## Slide 1: Energy efficiency and renewable energy in European industry
Aalborg University
17.03.2022
Webinar ”Vast Energy Efficiency and Renewable Energy Potentials within Industry in all EU countries”
Rasmus Magni Johannsen | rmj@plan.aau.dk

## Slide 2: IndustryPLAN tool overview
Industry sector modelling process
Data import
Scenario design
Review results
Export to EnergyPLAN
IndustryPLAN tool

## Slide 3: Energy savings cost curves
Cost of conserved energy BAT measures (3% discount rate)
~80% of energy savings from BAT technologies can be realised as cost saving measures
Top-end measures in non-ferrous metals (aluminium) and non-metallic minerals (cement) are expensive
Cost-curves based on technical lifetimes – industries may have other requirements
Cost-curves based on long-term natural gas price projections
  Current high prices would make EE improvements more attractive
Cost of conserved energy BAT measures (15% discount rate)
Notes: Note that non-ferrous metals extend beyond the graph to 114.98 EUR/GJ in 2030 and 114.09 EUR/GJ in 2050.
Based on long-term fuel price projections, including a natural gas price of 7-9 EUR/GJ. Currently natural gas is trading at 25-35 EUR/GJ, hence energy savings in sub-sectors supplied by natural gas would be even more attractive.
Taxes are not considered due to a socioeconomic perspective.

## Slide 4: Energy savings cost curves
Cost of CO2 abatement for BAT measures (3% discount rate)
~80% of the CO2 reduction potential can be realised as cost reducing measures
Differences from previous energy savings cost curves a result of fuel distribution across sub-sectors
  I.e. Iron and steel with a large share of low-cost coal with high CO2 emissions
Paper and pulp is largely electrified already, resulting in a low CO2 reduction potential
Cost of CO2 abatement for BAT measures (15% discount rate)
Notes: Note that non-ferrous metals extend beyond the graph to 1,934.60 EUR/t in 2030 and 1,760.69 EUR/t in 2050.
Based on long-term fuel price projections, including a natural gas price of 7-9 EUR/GJ. Currently natural gas is trading at 25-35 EUR/GJ, hence energy savings in sub-sectors supplied by natural gas would be even more attractive.

## Slide 5: 100% RE industry scenarios
Modelled scenarios
1
Low EE scenario
No increase in recycling
2
High EE scenario
High increase in recycling
3
High EE and electrification
High increase in recycling
Limited implementation of EE measures and electrification
Extensive biomass fuel shift
Extensive implementation of EE measures
Limited electrification
Medium biomass fuel shift
Extensive implementation of EE measures
Extensive implementation of electrification
Low biomass fuel shift
4
High EE, electrification and hydrogen
High increase in recycling
Extensive implementation of EE measures
Extensive implementation of electrification
Low biomass fuel shift
Extensive implementation of hydrogen measures

## Slide 6: 100% RE industry scenarios
Aggregate EU27+UK results
Final energy demand by scenario disaggregated by fuel type (EU27+UK).
Final energy demand by scenario disaggregated by industrial sub-sector (EU27+UK).
All scenarios (even low EE) can negate the increasing industry demand in the Frozen Efficiency scenario
Foregoing focus on EE and electrification results in large biomass demands
Hydrogen potential is (relatively) limited – especially before 2030
Electrification is by far the most important measure for enabling the industry transition
Chart: Final energy demand [PJ]
| 2015 | 2030 | 2050 | 2030 | 2050 | 2030 | 2050 | 2030 | 2050 | 2030 | 2050 | Base year | Frozen efficiency | Low EE | High EE | High EE and elec. | High EE and elec./H2
Coal and coal products | 1838438.729 | 1856452.3018 | 1392482.861 | 1731022.8316 | 0 | 1370657.0567 | 0 | 1356717.3774 | 0 | 1341741.1853 | 0
Oil products | 1248674.1757 | 1163678.4017 | 1014004.8212 | 1106431.9182 | 0 | 987119.7953 | 0 | 967698.742 | 0 | 926538.0672 | 0
Natural gas | 3490107.9839 | 3454140.7648 | 3638964.4503 | 3261937.5623 | 0 | 2932778.8463 | 0 | 2878805.0076 | 0 | 2760947.3393 | 0
Peat and peat products | 6975.5054 | 7407.516 | 394.5689 | 7066.3745 | 0 | 7008.4004 | 0 | 6756.0117 | 0 | 6597.7793 | 0
Biofuels and waste | 1084449.0832 | 1882894.6031 | 2614816.8129 | 1781345.3491 | 4855581.7789 | 1632710.7996 | 3232238.082 | 1599576.9484 | 2167968.4335 | 1541778.4867 | 940473.2468
Heat | 692558.609 | 1176233.0632 | 1572998.844 | 1116847.0822 | 866317.208 | 1025862.2783 | 648977.287 | 1000205.6036 | 421032.9507 | 961055.3064 | 135376.5098
Geothermal | 132.0587 | 282.2699 | 356.5247 | 268.9423 | 245.5678 | 242.4693 | 191.3191 | 242.4693 | 121.1193 | 226.2278 | 0
Electricity | 3562916.5963 | 3987761.3303 | 4315837.8052 | 3948735.8323 | 7330078.4116 | 3780831.4278 | 6272616.4231 | 3937904.3963 | 7082751.9867 | 3915022.747 | 6013132.7004
Hydrogen | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 254556.8583 | 1984169.8386
Chart: Final energy demand [PJ]
| 2015 | 2030 | 2050 | 2030 | 2050 | 2030 | 2050 | 2030 | 2050 | 2030 | 2050 | Base year | Frozen efficiency | Low EE | High EE | High EE and elec. | High EE and elec./H2
Chemicals | 2134035.035 | 2287643.6109 | 2314038.5252 | 2210725.4417 | 2131773.2507 | 2146639.2 | 2040146.4529 | 2139988.6044 | 2005744.7934 | 2125567.8683 | 1974865.2394
Foundries | 89293.4833 | 96148.4877 | 97501.0836 | 85895.1214 | 57657.1362 | 83117.0695 | 54807.1063 | 82599.1581 | 54807.1063 | 82599.1581 | 54807.1063
Iron and steel | 2045214.3798 | 2241495.6358 | 2223116.2198 | 2109142.1716 | 2438308.8136 | 1680536.6612 | 1389056.0585 | 1678472.1134 | 1381448.0325 | 1675336.5722 | 1414459.9136
Non-ferrous metals | 392049.2709 | 423889.6427 | 427690.7442 | 399664.3248 | 374706.7655 | 357738.1885 | 255255.3036 | 356958.4229 | 251332.7646 | 355398.8918 | 246217.5433
Non-metallic minerals | 1519881.0165 | 1815137.5329 | 1843017.6228 | 1703419.0184 | 1580003.83 | 1468827.2412 | 993212.1138 | 1461356.4564 | 959764.402 | 1449125.8407 | 911365.7205
Paper and pulp | 1468456.9653 | 1568859.4849 | 1611438.4716 | 1494944.2471 | 1098394.5423 | 1459052.8353 | 911931.6218 | 1434108.6267 | 699955.0232 | 1473578.9957 | 1263707.1934
Others | 4275322.5904 | 5095675.8557 | 6033054.021 | 4949865.5676 | 5371378.6279 | 4541299.8781 | 4509614.4543 | 4594423.1744 | 4318822.3682 | 4546856.6705 | 3207729.579
Notes: Note that energy system effects (outside of industry) are not considered. E.g. relevant for the production of hydrogen which with production through electrolysis would require significant electricity.

## Slide 7: 100% RE industry scenarios
Germany dominates European industrial energy demands – also in high EE scenarios
All countries can achieve substantial energy savings across all sub-sectors
“Others”-sub-sector constitutes significant portion of demand in most countries
  Leaves room for further disaggregation in future studies
Individual country results

## Slide 8: 100% RE industry scenarios
EE improvements can significantly reduce need for biofuels in all countries
H2 constitutes relatively small share of total demand, even in scenario with high implementation rate
  Mainly applied in chemicals and iron and steel sub-sectors
Individual country results

## Slide 9: Summary and conclusion
Four different pathways to 100% renewable energy in industry presented
  Extensive scope covering all EU countries and all industry sub-sectors in a bottom-up approach
Most energy and CO2 saving measures can be implemented at a negative cost – from a socio-economic perspective
  Need to leverage energy policy to comparably reduce business-economic payback times
A lacking emphasis on EE improvements and electrification results in extensive biomass consumption if pursuing 100% renewable energy
Potential for introducing hydrogen is limited – but also not needed in large-scale
EE improvements and the RE transition is pivotal in increasing security of supply and reducing natural gas dependency
Future integrated energy system modelling needs to consider the industry sector in greater detail – opening the “black box” of the industry sector

## Slide 10: Thank you for your attention!
Rasmus Magni Johannsen | rmj@plan.aau.dk
Aalborg University