## Slide 1: LESSONS FROM SEENERGIES FOR REPOWEREU
Notes: As a response to the European Commission’s 2050 decarbonization goals, sEEnergies uniquely considers all aspects of the Energy Efficiency (EE) First Principle. By applying it in sectors and markets, country-by-country and grid-by-grid, and by combining temporal and spatial analyses, sEEnergies will develop an innovative, holistic and research-based EE-modelling approach.
The aim of sEEnergies is to quantify and operationalize the potential for energy efficiency in buildings, transport, and industry. The project goes beyond state-of-the-art science-based knowledge and methods, as it combines sectorial bottom-up knowledge with hour-by-hour modeling of the energy systems and spatial analysis in the EU. Web: www.seenergies.eu Twitter: @sEEnergiesEU
In this webinar we will present an investment strategy roadmap based on an sEEnergies evaluation of the most critical energy efficiency improvements. This roadmap is complemented with knowledge from the existing best practices worldwide where energy efficiency measures are prioritised over supply-side investments.

## Slide 2: sEEnergies
Webinar 1
Webinar 3
Webinar 2
Webinar 4
Webinar 5
Webinar 6
Notes: Quantification and operationalization of the potentials for energy efficiency in buildings, transport, and industry.
The project combines sectorial bottom-up knowledge with hour-by-hour modeling of the energy systems and spatial analysis in the EU.
The projectincludesanalysisofnon-energybenefitsoftheenergyefficiencyfirstprinciplein thedifferent demandsectors
Combines the bottom-up knowledge needed to quantify and operationalize the EE potentials in buildings, transport and industry with temporal and spatial analyses to develop an innovative, holistic and research-based EE-modelling approach.

## Slide 3: Novelty
Investigated energy efficiency in each sector independently in each country
Investigated energy grid costs
Combined the energy sector scenarios and grid costs within an energy system analysis for each EU27+UK country
Notes: Novelty
Assess the impact of EE on sectoral and energy system level.
Quantify the synergies of EE and renewable energy systems.

## Slide 4: Sector scenarios and grid costs considered for each country
sEE 1.5
Energy supply technologies
Electrification+
Industry scenario 4
Building scenarios 1-24
Energy system design incl. grid costs
Country X
Example of energy system scenario
4 scenarios
4 scenarios
24 scenarios
Notes: Four 100% renewable scenarios with different combinations of BAT and innovative energy efficiency measures, material efficiency and fuel replacement
Gas grid sufficient since we are reducing gas for heating and for industry and new biogases can use current grid infrastrucutre and
  Biofuels
  Hydrogen
  Electrification & e-fuels
  Electrification+
  Low energy efficiency
  High energy efficiency
  High energy efficiency plus electrification
  High energy efficiency plus electrification/hydrogen
  Baseline building refurbishment (PRIMES 2050 Baseline ≈ 20% reduction from 2015)
  Baseline +20% additional savings
  Baseline +30% additional savings equivalent to PRIMES 1.5TECH

## Slide 5: Energy system analysis for each country
The EnergyPLAN tool was used to analyse the energy system performance of each country hour-by-hour over one year
Energy system performance was assessed based on
  Socio-economic cost of the energy system
  Renewable electricity capacity
  Level of electricity exchange with surrounding countries
  Balancing district heat production and demand
  Biomass consumption

## Slide 6: Method for scenario selection for a country
Here are a selection of 15 energy system scenarios analysed for a country
Three heat demand levels for buildings
The scenarios differ by splitting heat supply between district heat and private heating in different shares
For transport we are using the electrification+ scenario
For industry we are using Scenario 4 which is high energy efficiency + electrification/hydrogen use
Chart: Biomass TWh
| 70/30 | 60/40 | 50/50 | 40/60 | 30/70 | 70/30 | 60/40 | 50/50 | 40/60 | 30/70 | 70/30 | 60/40 | 50/50 | 40/60 | 30/70
 | 677.39 | 672.93 | 668.32 | 669.24 | 672.74 | 652.31 | 655.43 | 660.63 | 660.07 | 659.34 | 655.68 | 655.48 | 654.86 | 655.48 | 653.84
Chart: Million euro
| 70/30 | 60/40 | 50/50 | 40/60 | 30/70 | 70/30 | 60/40 | 50/50 | 40/60 | 30/70 | 70/30 | 60/40 | 50/50 | 40/60 | 30/70
Annualised costs | 230327 | 229264 | 228335 | 227811 | 227864 | 226651 | 226750 | 227116 | 227629 | 228544 | 228799 | 229371 | 230157 | 231248 | 232533
DH production | 217.3475 | 186.2978 | 155.2482 | 124.1986 | 93.1489 | 163.0106 | 139.7234 | 116.4361 | 93.1489 | 69.8617 | 133.6854 | 114.5875 | 95.4896 | 76.3917 | 57.2937
Baseline
Baseline+20%
Baseline+30%
We selected scenario 7
Biomass demand
Annualised costs and DH production
Notes: We consider costs, biomass demand, electricity exchange with surrounding countries. When scenarios are similar we select the conservative level of DH

## Slide 7: We analysed all other transport and industry scenarios
Electrification+ is the selected scenario for the EU27+UK
For industry we selected Scenario 4 high energy efficiency and electrification/hydrogen based on costs and biomass demand
Notes: Electricity demand, biomass and cost results for the four transport scenarios

## Slide 8: EU energy system primary energy demand
The final energy system configuration for each country was selected based on the performance assessment
An EU27+UK energy system was created from each of the selected countries
Notes: All fuel supplied internally
Novelty
Assess the impact of EE on sectoral and energy system level.
Quantify the synergies of EE and renewable energy systems.

## Slide 9: EU energy system primary energy demand
sEE1.5 is more energy efficient compared to 1.5TECH
Within limit of the reference biomass potential from the JRC ENSPRESO (2019)
  ≈ 3200 TWh biomass feedstock
Notes: Novelty
Assess the impact of EE on sectoral and energy system level.
Quantify the synergies of EE and renewable energy systems.

## Slide 10: Annualised costs at EU level
  sEE1.5 is more cost effective compared to 1.5TECH due largely to the removal of vehicles by more modal shift
  In the heating sector sEE1.5 has less energy savings (so lower costs) and better synergies due to district heat and use of excess heat
Notes: Difficult using available data but estimated costs for 1.5TECH and baseline
714 vs 1038 billion per year = 30% less vehicles costs

## Slide 11: Electricity production at EU level
Total electricity production is very similar to 1.5TECH
But different distribution
No nuclear therefore larger share of PV and onshore wind
Less offshore due the potentials shown in each country
This is the amount of renewable production needed but the split could be different
Also cheaper energy system due to more onshore wind and PV

## Slide 12: Heating supply
  Heat demand in existing buildings should be reduced by approximately 40%
  If 50% of heat is supplied with district heating significant amount of excess heat can be integrated
  Total excess heat utilised: 360 TWh or about 1/3 of the available
Total heat demand by source of heat

## Slide 13: Heating supply
District heating heat production
  Heat demand in existing buildings should be reduced by approximately 40%
  If 50% of heat is supplied with district heating significant amount of excess heat can be integrated
  Total excess heat utilised: 360 TWh or about 1/3 of the available

## Slide 14: Heat supply in different countries
EU: 50% district heat supply
Notes: 50% dh and 50% private which is 45% HP and 5% biomass boiler/electric heat
We cant go to 50/50 but reality is we have 5% remaining biomass boiler and electric heat

## Slide 15: Conclusions
Bottom up country level analysis with high level resolution on each energy sector
Compared with 1.5TECH the energy system is more energy and cost efficient with similar biomass demands
Moderate heat demand savings are required in existing buildings reduced by approximately 40% by 2050
Large share of district heating is required with waste heat integration and heat pumps
In transport its most beneficial and cost effective to implement highest level of electrification including e-roads
In industry its most beneficial and cost effective to implement highest level of BAT and innovative energy efficiency measures and electrification
Notes: , energy efficient urban development, and increased modal shift
Refurbishment rate should be increased to 1.1%
Direct electrification: most energy efficient of all known transport technologies
Well to wheel efficiency: BEV 73 % vs ICE 13 % (Transport and Environment)
Advancements in battery technology development
Advancements in power electronics
Low energy density of electric batteries as compared to HFO and Jet fuel
Dead Weight Tonnage and Maximum Take off Weight constraints for shipping and aviation respectively
Renewably sourced drop in electro-fuels with similar energy densities could be cleaner alternatives

## Slide 16: Q and A - Feedback